## Slide 1
Joe Saroufim
Giovanni Juan
RAMI AKL
Samer hayek
Presented to:
Dr. Jawad El Khoury
Path Clearing Rover
Mechatronics System Design
MCE410 Project
Fall 2021

## Slide 2
Outline:
Project Description
Electric Circuits
Tasks Achieved
Hardware Overview

## Slide 3
Line Tracking
Follows a certain black path
Obstacle detection
Stops at a fixed distance from the obstacle
Smart Reaction
Go left
Go right
Push
Project Description

## Slide 4: Hardware Overview
Power Bank
5V , 2A
Camera
DC Motors (6V)
Motor Driver
Distance Sensor
Batteries (3.7V, 3400mAh supply each)
Two IR Sensors
Servomotor
Raspberry Pi 3 B+

## Slide 5: Infrared Line Sensors
White: Output HIGH
Black: Output LOW

## Slide 6: Driving Motors
Motors connected in parallel on each side
Enable pins: PWM signal
IN1, IN2, IN3 and IN4 for switching directions
All control pins on motor driver are connected to GPIO on Raspberry Pi

## Slide 7: Servo Motor & Distance Sensor
Servo motor:
Servo motor is used for pushing obstacle
Powered by 5V pin on raspberry pi
Ultrasonic:
Ultrasonic sensor reads the distance from the obstacle
VCC pin for powering the ultrasonic sensor
Echo is the receiver pin
Trig is the emitter pin

## Slide 8: Following the Line
1
2
3
4
5
Stage | Right Sensor | Left Sensor | Motion
1 | 1 | 1 | Forward
2 | 1 | 0 | Right
3 | 0 | 1 | Left
4 | 1 | 1 | Forward
5 | 0 | 0 | Stop
IR Sensors

## Slide 9: Approaching the Object
30 cm
13 cm
Distance Sensor
When the distance sensor reads a distance that is less than 40 cm, the rover stops.
The rover then moves forward gradually until the sensor reads a distance of 13 cm.

## Slide 10: Reading the Sign
13 cm
string
At a distance of 13 cm, the camera can detect text properly
Based on the detected text, the program decides to avoid or push the sign.
Tesseract
Python Library
“Right”
“Left”
“Push”
Sample image taken by the camera

## Slide 11: Avoiding the Object
The rover stops following the line and executes the sequence below:
Right IR Sensor
Backwards
Right
Forward
Left
Forward
The rover resumes line following when the right sensor detects the line
1
2
3
4
5
6
7

## Slide 12: Pushing the Object
The arm of the servomotor rotates to push the object
The rover then resumes line following

## Slide 13: Thank you!